## Slide 1: StorScore system for SSD qualification
Dr. Laura Caulfield
Mark Santaniello

## Slide 2: Outline
Introduction
  Who we are
  Unique needs & opportunities
  Motivation
Background
  SSD testing “gotchas”
How it works
  Recipes: define the test suite
  Scores: compare devices and summarize performance
  Endurance: measurement of write amplification
Demo

## Slide 3: Introduction

## Slide 4: Who we are
Cloud server infrastructure engineering
  Designers of Open Cloud Server
  Part of the Open Compute Project
  http://opencompute.org

## Slide 5: Unique needs & opportunities
Microsoft’s platform
Variety / quantity of workloads
Flexibility to modify stack
Co-design SSD & apps
Wide variety of expertise
Additional metrics
System development (Web search, hosted cloud, etc.)
SSD vendors

## Slide 6: Motivation
Need for a component-level storage test (AVL/QCL)
Problems with 3rd-party testing services
  Want test results under Windows, not Linux
  Need results in our server, not a “reference platform”
  Desire to share results with component vendors
Existing tools are insufficient (Iometer, etc.)
  GUI = difficult to automate properly, therefore error-prone
  Microsoft-specific tests (SMART injection)
  Cloud metrics (QoS via 5-nines percentile latency)
  Methodology is critical when testing SSDs

## Slide 7: Background

## Slide 8: SSD gotcha – initial performance
NAND must be erased before it can be programmed
When fresh-out-of-box, all NAND is already erased
  Drive contains more NAND than the user-visible space
  Overprovisioned (OP) space, typically 7% or 28%
This is an unnatural and ephemeral state
  Reads short-circuit if block state is erased (never go to media)
  Sustained writes will eventually require garbage collection (GC)
StorScore initializes by writing the entire SSD 2x
  Every user-exposed LBA is written twice
  Virtually guaranteed to cover any OP space

## Slide 9: SSD gotcha – history effect
Previous workload affects current workload
Transition phase can take hours
Main causes
  FTL map fragmentation (ex: random  sequential)
  Concurrent garbage collection activity (ex: 100% write  0% write)
Workload A
Workload B
Steady-state
Transition
Steady-state

## Slide 10: SSD gotcha – history effect, continued
Consistent workload will eventually reach steady-state
1st Pass, 3.5 hours
  30 – 100 MB/sec
2nd Pass, 30 minutes
  ~220 MB/sec
Chart: 1MB Sequential Writes on Fragmented SSD
1st Pass
2nd Pass

## Slide 11: SSD gotcha – detecting steady-state
StorScore includes precondition.exe
  Always drives to steady-state before measuring performance
  Method: rolling linear regression, detect near-zero slope
StorScore performs all sequential tests before any random tests
  Minimizes fragmentation and therefore time required to achieve steady-state

## Slide 12: SSD gotcha – entropy of written data
Some controllers can compress on-the-fly
  Customer data is often compressible
  Entropy has a big impact on performance and endurance
StorScore supports variable compressibility
  Uses incompressible data by default
  Allows use of compressible data in 10% increments
Chart: Random Write Throughput: 0%, 20%, 50%
| 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | 4 | 8 | 16 | 64 | 1024 | 2048
Kingston E75 (Cirrus) 480GB 0% | 6.79 | 8.46 | 8.8 | 8.71 | 9.11 | 10.58 | 17.57 | 17.68 | 18.27 | 16.97 | 21.6 | 28.06 | 18.73 | 17.75 | 19.79 | 18.15 | 21.87 | 27.97 | 20.13 | 19.91 | 20.83 | 19.86 | 22.37 | 27.7 | 20.11 | 19.89 | 20.03 | 19.93 | 20.46 | 18.64 | 19.97 | 19.99 | 20.09 | 19.76 | 20.31 | 19.23
Kingston E75 (Cirrus) 480GB 20% | 12.22 | 18.01 | 25.07 | 29.17 | 27.72 | 31.11 | 57.9 | 58.82 | 58.65 | 61.6 | 61.36 | 62.3 | 63.99 | 65.58 | 65.46 | 66.22 | 67.94 | 67.63 | 81.01 | 80.58 | 81.09 | 80.99 | 81.89 | 82.79 | 91.2 | 90.62 | 90.11 | 89.98 | 89.77 | 90.01 | 89.83 | 90.04 | 89.91 | 89.9 | 89.53 | 89.94
Kingston E75 (Cirrus) 480GB 50% | 14.76 | 24.06 | 36.25 | 52.49 | 61.81 | 61.39 | 113.17 | 155.87 | 155.65 | 157.25 | 159.09 | 164.12 | 163.61 | 182.67 | 182.97 | 184.58 | 184.42 | 186.99 | 241.95 | 243.6 | 243.49 | 243.26 | 243.5 | 243.87 | 268.78 | 278.42 | 278.17 | 277.47 | 277.58 | 277.47 | 275.78 | 275.28 | 274.8 | 274.74 | 274.63 | 274.98

## Slide 13: How it works

## Slide 14: Recipes – a single test
The entire contents of single.rcp
Reference the file from the cmd line: C:\>StorScore --recipe=single.rcp
Reads like English

## Slide 15: Recipes – a matrix of tests
Mimics test designer’s whiteboard sketch
Include statements combine test files
Full functionality of Perl

## Slide 16: Results parser
Raw output files  one Excel file
Detects, highlights outliers
Easy pivot tables & graphs
Still too much data
  5,232 files x 23 metrics = 120k data points
Display Name | Write Mix | Access Size (kB) | Access Type | Queue Depth | Bandwidth (MB/s) | Average Latency (ms)
Device A | 100% | 16 | random | 1 | 54.32 | 1.04
Device B | 100% | 16 | random | 1 | 15.05 | 0.29
Device A | 30% | 16 | random | 1 | 20.01 | 1.39
Example policy:
Bandwidth matters a lot, latency matters a little
Device A scores 72/100
Device B scores 65/100
24 SSDs
x 218 workloads
5,232 files

## Slide 17: Putting the “score” in StorScore
Display Name | Write Mix | Access Size (kB) | Access Type | Queue Depth | Bandwidth (MB/s) | Average Latency (ms)
Device A | 100% | 16 | random | 1 | 54.32 | 1.04
Device B | 100% | 16 | random | 1 | 15.05 | 0.29
Device A | 30% | 16 | random | 1 | 20.01 | 1.39
Goal
  Enable data-driven decisions throughout the company
Reduce data to 1 score / drive
Method
  A weighted average of all the metrics for each workload
Bandwidth (MB/s) | Average Latency (ms)
Z_AX0 | Z_AX1
Z_BX0 | Z_BX1
Z_AY0 | Z_AY1
Step 1: Convert each value to z-score

## Slide 18: Calculating z-scores
Drive: A
Workload: X (4k, rand, QD1, 100% writes)
Metric: 0 (Read Latency)
One z-score per data point
Positive = better than average
Negative = worse than average
Based on cohort of drives
A z-score (or standard score) is the number of standard deviations from the mean
zAX0
Good
Bad
Distribution of
all drives
workload X
metric 0
Drive A

## Slide 19: Applying scoring policies
zA(n+m)i
50%
Throughput Metrics
Latency Metrics
50%
zA(n+m)j
+
=
General Policy:
70 / 100
zAn(i+j)
5 x
70/30 Read/Write Mix Workloads
100% Read & 100% Write Workloads
1 x
zAm(i+j)
+
=
Policy to Favor Mixed Workloads:
65 / 100
Can apply multiple policies at once
Can use any kind of weight system (stay consistent within policy)
x
x
Drive A
Wkld range 0 to (n+m)
Metric range 0 to i
Score for Drive A

## Slide 20: Scores
H is so close, and they’ve got a great price. How do we tweak the drive or application to make it work?
Chart: Device
| A | K | M | L | I | H | J | F | D | G | B | C | E | N
Score | 83.9787 | 73.8028 | 70.6888 | 69.9978 | 69.5282 | 65.24 | 62.1678 | 61.967 | 60.0118 | 57.4066 | 56.6263 | 51.201 | 27.9343 | 21.9318
A is best-in-class
If you’ve been using L, A-I will be comparable or better
E & N are stragglers

## Slide 21: Scores’ breakdown
H is so close, and they’ve got a great price. How do we tweak the drive or application to make it work?
Chart: Device
| A | K | M | L | I | H | J | F | D | G | B | C | E | N
Random Writes | 6.4858 | 6.7694 | 3.789 | 3.4673 | 5.8427 | 3.8388 | 5.167 | 3.8035 | 3.4203 | 3.5798 | 3.5709 | 3.4532 | 1.1202 | 0.38835
Random Mix | 33.9535 | 28.7849 | 25.0614 | 23.6078 | 31.1455 | 23.4848 | 26.0327 | 23.0097 | 22.5014 | 22.2031 | 22.592 | 20.5349 | 6.8018 | 1.3952
Random Reads | 4.7287 | 3.8506 | 3.311 | 7.0294 | 3.6357 | 5.9084 | 3.9335 | 5.5798 | 3.4946 | 4.9365 | 3.9596 | 4.009 | 3.3287 | 2.7463
Sequential Writes | 5.1542 | 5.0666 | 3.6616 | 5.3799 | 6.4618 | 5.5906 | 4.4797 | 4.755 | 2.5288 | 4.2959 | 5.0229 | 5.0589 | 1.53 | 1.6263
Sequential Mix | 30.3383 | 26.8454 | 30.0979 | 24.6748 | 17.2571 | 20.2028 | 20.6333 | 18.7318 | 23.5668 | 16.2756 | 18.8769 | 15.4373 | 10.9743 | 11.3759
Sequential Reads | 3.3181 | 2.486 | 4.7679 | 5.8387 | 5.1852 | 6.2146 | 1.9216 | 6.0871 | 4.4999 | 6.1157 | 2.604 | 2.7076 | 4.1792 | 4.3998
Answer: Drive should improve random mix (not seq. mix), or
App should favor sequential mix (not random mix)
Notes: Quick Answer
Then: “This is a super useful chart – I’ve personally spent hours staring at these. 95% of the time is exploring new questions, not in looking for the answers”

## Slide 22: SSD failure mechanism: writes
Write Amplification Factor Workload Dependent, Vendor Reported, Implementation Specific
Drive Writes Per Day (DWPD)
Total Bytes Writes (TBW)
Drive Writes (DW)
SSD
Controller
NAND
NAND
NAND
NAND
Host Writes
Controller Writes
=
x
P/E Cycles
Total Drive Writes
New Telemetry
SMART “Controller Writes”
Reported in units of sectors or GB
1,700 workloads in 4.7 months
Previously Available
SMART “Media Wear Indicator”
Reported in units of 1% (300 TB for 30k, 1TB drive)
4.7 months for 1 workload
Program / Erase Cycles (P/E Cycles, or PEC)
Write / Erase Cycles (W/E Cycles)
Notes: Slowest workload: 64k random read/write mix, QD 1 (768 MB/s to the flash)

## Slide 23: Endurance Results
Chart: Drive Writes Per Day (3 years)
Device H | 0.55489 | 0.55596 | 0.5568 | 1.1005 | 1.0943 | 1.0981 | 1.1665 | 1.1707 | 1.1811 | 1.2799 | 1.2701 | 1.2673 | 1.3753 | 1.3487 | 1.3826 | 1.3707 | 1.3528 | 1.3239 | 3.1425 | 3.0551 | 2.7327 | 3.3353 | 3.3343 | 3.3329 | 3.3336 | 3.3355 | 3.3313 | 3.3347 | 3.3341 | 3.3318 | 3.2307 | 3.2314 | 3.2296 | 3.2251 | 3.229 | 3.2285
Device J | 3.0944 | 3.0966 | 3.095 | 3.0941 | 3.0969 | 3.0985 | 3.0961 | 3.0996 | 3.0999 | 3.0905 | 3.0937 | 3.0871 | 3.1493 | 3.1476 | 3.1383 | 3.1881 | 3.1946 | 0.42072 | 16.4383 | 16.4383 | 13.9096 | 14.0995 | 16.4384 | 7.4007 | 15.571 | 16.2574 | 16.4384 | 14.5152 | 16.4384 | 16.4384 | 16.0959 | 3.396 | 16.4384 | 14.5531 | 9.4822 | 16.4384
Queue Depth
Write Size (kB)
Access Pattern
Reported Range

## Slide 24: Endurance Results
Chart: Drive Writes Per Day (3 years)
Device H | 0.55489 | 0.55596 | 0.5568 | 1.1005 | 1.0943 | 1.0981 | 1.1665 | 1.1707 | 1.1811 | 1.2799 | 1.2701 | 1.2673 | 1.3753 | 1.3487 | 1.3826 | 1.3707 | 1.3528 | 1.3239 | 3.1425 | 3.0551 | 2.7327 | 3.3353 | 3.3343 | 3.3329 | 3.3336 | 3.3355 | 3.3313 | 3.3347 | 3.3341 | 3.3318 | 3.2307 | 3.2314 | 3.2296 | 3.2251 | 3.229 | 3.2285
Device J | 3.0944 | 3.0966 | 3.095 | 3.0941 | 3.0969 | 3.0985 | 3.0961 | 3.0996 | 3.0999 | 3.0905 | 3.0937 | 3.0871 | 3.1493 | 3.1476 | 3.1383 | 3.1881 | 3.1946 | 0.42072 | 16.4383 | 16.4383 | 13.9096 | 14.0995 | 16.4384 | 7.4007 | 15.571 | 16.2574 | 16.4384 | 14.5152 | 16.4384 | 16.4384 | 16.0959 | 3.396 | 16.4384 | 14.5531 | 9.4822 | 16.4384
Queue Depth
Write Size (kB)
Access Pattern
Reported Range
Not all sequential workloads achieve High Endurance
Identify problem workloads

## Slide 25: Demo

## Slide 26: Thanks!
Download StorScore
  http://aka.ms/storscore
Questions?

## Slide 27
© 2013 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.